## Slide 1
Early-Warning Prediction of Asthma Exacerbations
using wearable and digital-health data
Bahaa Hamdan | Tarek El Moura | Anthony John Kanaan
EECE 693 Neural Networks / Deep Learning - Spring 2026
AUB
American University
of Beirut
Public AAMOS-00 asthma monitoring dataset
Core claim
We built a patient-safe early-warning pipeline that predicts pre-exacerbation risk from multimodal historical signals. The best held-out signal was promising, but statistically fragile because the test set contained only four positive events.
Not deployment-ready
needs larger prospective validation
CLINICAL TASK
Goal
Predict upcoming asthma exacerbation risk before clinically meaningful worsening, using only historical data available before onset.
Why hard?
Rare positives: event windows are sparse.
Patient-specific baselines and triggers.
Missingness reflects behavior, adherence, charging, and device dropout.
Primary selection metric: validation PR-AUC
DATA & LABELS
AAMOS-00 multimodal sources
Smartwatch
heart rate, steps, activity, intensity
Smart inhaler
reliever medication timestamps
Peak flow
PEF readings
Questionnaires
daily / weekly symptom evidence
Environment
weather and exposure context
Patient info
static demographic / clinical descriptors
Event-episode labeling
Positive: historical window immediately before probable event onset.
Negative: stable periods with no event/positive-week overlap.
Washout: post-event recovery days excluded from stable-negative sampling.
SAMPLING GRID
Event threshold
2, 3, 4
History length
3, 7, 14 days
Washout
0, 7, 14 days
Example T3/L14/W14
53 pos / 1,071 neg
FULL PIPELINE
Every model is evaluated under the same patient-level split and validation-first selection discipline.
1
Raw
AAMOS-00
2
Clean +
standardize
3
Event
episodes
4
Lookback
features
5
Patient-safe
split
6
Tune
models
7
Validate
PR-AUC
8
Final held-
out test
Label timing
Input history
E-L ... E-1
Event onset
E
Event
episode
Post-event washout
excluded negatives
Model families
Classical
LR - RF - XGBoost
Sequence DL
RNN - GRU - LSTM - CNN
Selection
validation PR-AUC first
Safeguards
gap - Brier - leakage - seeds
EVALUATION DISCIPLINE
Metric
PR-AUC primary; ROC-AUC, F1, recall, Brier as companions
Threshold
chosen on validation only; applied unchanged to test
Split
patient-level train / validation / test separation
Stress tests
label-shuffle leakage probe, sensor ablation, bootstrap CIs, multi-seed DL
HELD-OUT TEST RESULTS
Validation-selected v2 second run
Model
T/L/W
PR-AUC
ROC-AUC
F1
Test
RF
4/14/14
0.555
0.934
0.667*
325 (4+)
XGB
3/14/14
0.526
0.875
0.308
324 (4+)
RNN
3/14/14
0.261+/-.148
0.902+/-.057
0.000
324 (4+)
LR
4/14/0
0.022
0.615
0.041
350 (4+)
*RF value is validation-tuned F1. XGB F1 shown is untuned test F1; tuned F1 was lower.
Wide uncertainty
RF PR-AUC 95% CI: 0.033 to 1.000 because the held-out test set had only four positives.
Takeaway
Promising rank signal exists, but clinical reliability is not established.
INTERPRETING MULTIMODAL SIGNAL
All-sensor tabular RF produced the strongest validation-selected held-out result.
Ablation patterns were not monotonic; sensor-source importance is not cleanly separable.
Questionnaire-derived predictors may be close to symptom-based labels and must be checked for proxy-label effects.
High accuracy alone is not meaningful in this rare-event setting.
Scientific reading: best signal found, not deployment readiness.
LIMITATIONS & NEXT STEPS
Small cohort
~22 enrolled; 20 modeled users after preprocessing
Few events
test positives often 4 or fewer
Stability
leakage probes near-random overall, but individual configs unstable
Next
patient-level CV, raw-minute/downsampled representations, external validation
What we contributed
RIGOROUS SAMPLING
event-episode windows, post-event washout, patient-safe splits
MODEL COMPARISON
LR/RF/XGB + RNN/GRU/LSTM/CNN under the same validation rule
TRUST CHECKS
calibration, train-val gap, leakage probes, ablation, bootstrap CIs
HONEST RESULT
promising signal with explicit uncertainty and non-deployment caveat
Code and results: v2 event-episode protocol - final numbers from v2_results_second_run/v2/tables - Poster generated as editable PowerPoint
A+ target: clear pipeline, credible validation, restrained claims